## Slide 1: 2014 TWG USACE Field Report
LySanias Broyles
Rock Island District
United States Army Corps of Engineers
LySanias.D.Broyles@usace.army.mil
06-MAY-2014

## Slide 2: GOES
Majority of Corps’ 2,000+ platforms transmit hourly with 5 – 10 second transmit windows
  A few DCP’s left to upgrade to HDR
  Some exceptions
    St. Louis District uses ½ hour transmissions throughout
    Rock Island uses ½ hour transmissions at Mississippi and Illinois Locks (1-minute using network DCP’s)
  Would like to transmit more frequently at strategic locations
    Downstream from projects (locks, reservoirs, etc.)
    Around or near municipalities
    Areas with propensity for flash flooding or other rapidly changing phenomena
    Possible secondary transmission for event/threshold driven (e.g. ALERT type) stations

## Slide 3: Software
Funded Enhancements
  Microcom DAMS-NT
    DRGS client limit increase
      Increased from 10 to 50 clients can connect to each of the East and West DAMS-NT servers
      USACE LRGS’s connect as clients
        MVR DAMS-NT DRGS systems collect all USACE DCP transmissions
  Sutron/Ilex DCP Monitor Web Service
    Accesses underlying databases and repositories driving the DCP Monitor web application
    Implements several parameterized URL method calls
    Returns consistent XML constructs
      Full performance parameters, meta data, raw and decoded data, etc.
    http://38.100.141.26/dcpmon/resources/platform/getFullPerformanceParams?dcpAddress=ED001298&name=155

## Slide 4
<Platforms>
<Platform DcpAddress="CE5B7D7A">
<DcpName>KERN_RVR_BLW_MAIN_DAM</DcpName>
<Agency>sce</Agency>
<FirstXmiTime>00:21:10</FirstXmiTime>
<Channel type='self--‐timed'>88</Channel>
<TxInterval>01:00:00</TxInterval>
<TxWindow>5</TxWindow>
<BaudRate>300</BaudRate>
<Preamble>S</Preamble>
<Messages numMessages=1>
<Message Time="12/27/2013 19:21:12 UTC">
<XmitStart>19:21:11.284</XmitStart>
<XmitEnd>19:21:13.793</XmitEnd>
<WindowStart>19:21:10</WindowStart>
<WindowEnd>19:21:15</WindowEnd>
<FailureCode>G</FailureCode>
<SignalStrength>38</SignalStrength>
<FrequencyOffset>+1</FrequencyOffset>
<MessageLength>66</MessageLength>
<DRGSCode>XE</DRGSCode>
<ModulationIndex>N</ModulationIndex>
<BatteryVoltage>N/A</BatteryVoltage>
</Message>
Example DCP Monitor Web Service Output

## Slide 5: Software
Funded Enhancements (cont’d)
  Cove Open DCS
    “Ease of Use” enhancements to DECODES Script Editor
    LRGS DOMSAT DPC OPEN DCS compatibility
      Facilitates connectivity between DOMSAT Protocol Converter and Open DCS LRGS
    DbImport
      Creates required directory structure upon invocation
      Simplifies use with DbExport and DECODES synchronization/mobility

## Slide 6: Hardware/Software
Future Enhancements
  Improved DECODES presentation groups
  Improved LRGS search criteria editor
  DECODES routing global property overrides
    Override system specific decodes.properties parameter values
      E.g. Command-line, global properties file/attributes
    Essentially, run same spec’s on any system
      Effective routing spec portability
  First of redundant LRIT receivers installed FY14 at Rock Island
  Microcom DRGS upgrades to handle HDR CS1/CS2 switching FY14 at Rock Island
  2-way GOES communication

## Slide 7: Software
Open DCS or DCS Toolkit?
  Cove Open DCS: open source
  Sutron DCS Toolkit: includes both open source and proprietary components
  Both can communicate with each other
    Both variants running on Corps data acquisition servers for network only data acquisition
  Both share a similar codebase
  Diverging development paths
    Different enhancements already funded for both
  Corps will decide which to be included in Water Management Enterprise Server (WMES) standard configuration
    Selection will not preclude use of the non-standard DCS software on other Corps servers
    Compatibility between DCS Toolkit and Open DCS
      Imperative for partnering within USACE and with other agencies
    Benefit from enhancements to WMES DCS funded by other districts
    Future development and maintenance support