## Slide 1
April 28, 2016
NOAA Satellite and Information Service | Office of Satellite and Product Operations
GOES DCS Assignment Policies
Kay Metcalf, NOAA GOES DCS Program Manager

## Slide 2
Assignment Policies
2
The Current GOES DCS Transmitter Standard is HDR CS2
The Current Standard Transmission Rate is 300 bps
  Exceptions are made for extremely long messages for 1200 bps
The Current Transmission Period is 1 hour (yes, I know, you all want 15 minutes…exceptions to follow)
  Users with strong justifications for faster transmissions may be granted more frequent transmissions
  Users with Tide Gages being used for Tsunami Monitoring are transmitting every 5 minutes
  Users in some flash flood prone areas are granted every 30 minutes or every 15 minutes
  Some large users are being granted every 15 minutes in return for blocking assignments on adjacent channels and ONLY using CS2 transmitters
    Hope to speed up CS2 transition
    Adjacent channels required to open up new between channels

## Slide 3
Assignment Policies
3
The Current Standard Window is 5 seconds or 10 seconds
We strongly encourage use of Pseudo Binary, but understand it is difficult to process for some users…and doesn’t provide nice easy to read format
The key to optimize transmissions is efficient system use
  Compression whenever possible
  Don’t send redundant information
  Try not to send verbose messages
Only CS2 transmitters should be deployed at this time
All 100 bps transmitters should be removed
All Random transmissions should be sent at 300 bps
All version 1 300 bps transmitters can be used for 10 years…no need to remove them yet
  We may eventually begin to move version 1 transmitters to different channels to free up new channels

## Slide 4
GOES DCS Contact Information
4
Kay Metcalf
  GOES DCS Program Manager
  kay.metcalf@noaa.gov
  301-817-4558
Letecia Reeves
  GOES DCS Customer Service
  Letecia.reeves@noaa.gov
  301-817-4563
URL
  http://noaasis.noaa.gov/DCS
  https://dcs1.noaa.gov
  https://dcs2.noaa.gov
  https://dcs3.noaa.gov
  https://dcs4.noaa.gov